## Slide 1
Fuzzy Logic Controller
Soft Computing Applications
12.02.2018
1 / 34

## Slide 2: Applications of Fuzzy Logic
Soft Computing Applications
12.02.2018
2 / 34

## Slide 3: Fuzzy Systems : Fuzzy Logic Controller
Concept of fuzzy theory can be applied in many applications, such as fuzzy reasoning, fuzzy clustering, fuzzy programming etc.
Out of all these applications, fuzzy reasoning, also called ”fuzzy logic controller (FLC)” is an important application.
Fuzzy logic controllers are special expert systems. In general, a FLC employs a knowledge base expressed in terms of a fuzzy inference rules and a fuzzy inference engine to solve a problem.
We use FLC where an exact mathematical formulation of the problem is not possible or very difficult.
These difficulties are due to non-linearities, time-varying nature of the process, large unpredictable environment disturbances etc.
Soft Computing Applications
12.02.2018
3 / 34

## Slide 4: Fuzzy Systems : Fuzzy Logic Controller
A general scheme of a fuzzy controller is shown in the following figure.
Fuzzy rule base
Fuzzy inference engine
Defuzzification module
Fuzzification module
Process to be controlled
Input
Output
actions
Conditions
Fuzzy Controller
Figure 1
Soft Computing Applications
12.02.2018
4 / 34

## Slide 5: Fuzzy Systems : Fuzzy Logic Controller
A general fuzzy controller consists of four modules:
1
a fuzzy rule base,
2
a fuzzy inference engine,
3
a fuzzification module, and
4
a defuzzification module.
Soft Computing Applications

## Slide 6: Fuzzy Systems : Fuzzy Logic Controller
As shown in Figure 1, a fuzzy controller operates by repeating a cycle of the following four steps :
1
Measurements (inputs) are taken of all variables that represent relevant condition of controller process.
These measurements are converted into appropriate fuzzy sets to express measurements uncertainties. This step is called fuzzification.
The fuzzified measurements are then used by the inference engine to evaluate the control rules stroed in the fuzzy rule base. The result of this evaluation is a fuzzy set (or several fuzzy sets) defined on the universe of possible actions.
This output fuzzy set is then converted into a single (crisp) value (or a vector of values). This is the final step called defuzzification. The defuzzified values represent actions to be taken by the fuzzy contoller.
2
3
4
Soft Computing Applications

## Slide 7: Fuzzy Systems : Fuzzy Logic Controller
There are two approaches of FLC known.
1
Mamdani approach
2
Takagi and sugeno’s approach
Mamdani approach follows linguistic fuzzy modeling and characterized by its high interpretability and low accuracy.
On the other hand, Takagi and Sugeno’s approach follows precise fuzzy modeling and obtains high accuracy but at the cost of low interpretably.
Soft Computing Applications